## Slide 1: CYBR644 – Cyber Practitioner Lab
Spring 2024
University of Maryland, Baltimore County
Michael Hennick

## Slide 2: Discord Reminder
This class uses a Discord Server to facilitate “classroom discussion” during lecture and between classes
Please follow the link below to join the server and I’ll add everyone to the role for this semester’s class.
You can also request a “private” channel for your group so you can work and share information “amongst yourselves” and not on the classroom wide “general” channel.
https://Lairnet.link/Discord

## Slide 3: Review
Know the Security Triad elements.
Be familiar with the elements of risk.
Describe the modes of ethical hacking.
Be familiar with the different types of security tests.
Describe the difference between hackers, crackers, and ethical hackers.
Be familiar with test phases of ethical hacking.
Know the laws and regulation governing cybercrimes.
What is Ethical Hacking and why do we do it?
Understand key command line tools and what the information tells you in each “Cyber Security” perspective
1. IPCONFIG/IFCONFIG
2. PING
3. NETSTAT
4. ARP
5. TRACEROUTE/TRACERT
6. NET [USE, VIEW, etc]

## Slide 4: Overview of the course
Week 01 – Introduction, Ethical Hacking Basics, Ethics, Law
Week 02 – Technical Foundations of Hacking
Week 03 – Reconnaissance, Social Media
Week 04 – Scanning and Probing
Week 05 – Vulnerability Identification
Week 06 – Exploiting Weaknesses
Week 07 – Class Presentations / Review for Exam
Week 08 – Spring Break
Week 09 – Midterm Exam
Week 10 – Privilege Escalation, Maintaining Access
Week 11 – Malware, Covering your Tracks
Week 12 – The Web
Week 13 – Wireless and Mobile Security
Week 14 – Physical Security, Social Engineering, and Security Policies
Week 15 – Class Presentations / Review for Exam
Week 16 – Final Exam

## Slide 5: Attacker’s Methodology
  Attackers follow a fixed methodology that can be divided into six steps:
    Performing reconnaissance
    Scanning and enumeration
    Gaining access
    Escalation of privilege
    Maintaining access
    Covering tracks and placing backdoors

## Slide 6: Reconnaissance and Footprinting
The first pre-attack phase
Systematic attempt to collect as much information about the target as possible:
  PASSIVE information gathering
Reconnaissance techniques:
  Dumpster diving
  Social engineering
  Internet research

## Slide 7: Scanning and Enumeration
Second pre-attack phase.
Scanning is actively trying to connect to the system and get a response and identify open ports.
Enumeration is in-depth information gathering about the target:
  Open shares
  User accounts information
  Software versions
Considered ACTIVE information gathering.

## Slide 8: Gaining Access
  The attacker moves from probing the network to attacking it.
  Access can be gained using a variety of techniques:
    Open wireless connection
    Unsecured system
    System vulnerability
    Web applications vulnerabilities
    Backdoors
    Using social engineering techniques to get network access information

## Slide 9: Escalation of Privilege
Attackers try to gain administrative access by escalating their privilege.
  By exploiting a vulnerability or a bug in the system or an application
After the privilege escalation attackers have full control over the system and network.

## Slide 10: Maintaining Access
Attackers use various techniques to maintain access to the system:
  Stealing additional passwords
  Placing rootkits
  Using sniffers

## Slide 11: Covering Tracks
Attacker try to erase all evidence from their activities:
  Modifying log files to cover tracks
  Hiding files and folders
  Using Alternate Data Streams (ADS)
  Using rootkits
A backdoor could be used for gaining access to the system again.

## Slide 12: Attack Methodology
Reconnaissance/Open Source Intelligence
What network space does a target use?
What does the internet know about a target?
What information about my target is in social media sites?
2. Scanning and Enumeration
What hosts are online within a target’s network space?
What protocols are the hosts using?
What Operating Systems/Applications are running?
(2.5. Vulnerability Identification)
What is potentially exploitable on these target systems?
What are means for attack for this target?
3. Gaining Access/Exploitation
Exploiting the vulnerabilities to get access to the target, or taking advantage of other weaknesses
4. Escalation of Privilege
Exploiting the vulnerabilities to get access to the target
5. Maintaining Access/Exfiltration of Data
Create a legitimate method of accessing the system
“Smash-and-grab”
6. Cover Tracks
Removing log files/history

## Slide 13: The Ethical Hacker’s Process
Follows a similar process as the attacker.
Strives to do no harm.
The goal is to assess the organization’s strengths and weaknesses and develop a security methodology.
Five steps in security methodology:
  Assessment
  Policy development
  Implementation
  Training
  Auditing

## Slide 14: Additional Methodologies
NIST 800-115 (Information Security Testing & Assessment)
Operational Critical Threats, Assets, and Vulnerability Evaluation (OCTAVE)
Open Source Security Testing Methodology Manual (OSSTMM)
Penetration Testing Execution Standard (PTES)
Penetration Testing Framework (PTF)
And more…..

## Slide 15: OSI Model
Describes the flow of communications in a network environment
Seven layers
  Application
  Presentation
  Session
  Transport
  Network
  Data link
  Physical

## Slide 16: OSI Model

## Slide 17: OSI Model

## Slide 18: OSI vs TCP/IP Model

## Slide 19: TCP/IP Protocol Model
The standard for Internet and network communications
Consists of four layers:
  Application (7,6,5)
  Host-to-host (4)
  Internet (3)
  Network access (2,1)
Contains multiple protocols but there are four main ones:
  Internet Protocol (IP)
  Transmission Control Protocol (TCP)
  User Datagram Protocol (UDP)
  Internet Control Message Protocol (ICMP)

## Slide 20: Application (7,6,5) Layer
Responsible for application support
Protocols:
  File Transfer Protocol (FTP)
  Telnet
  Simple Mail Transfer Protocol (SMTP)
  Domain Name Service (DNS)
  Trivial File Transfer Protocol (TFTP)
  Hypertext Transfer Protocol (HTTP)
  Simple Network Management Protocol (SNMP)

## Slide 21: Application (7,6,5) Layer

## Slide 22: Application (7,6,5) Layer

## Slide 23: Host–to–Host / Transport (4) Layer
Provides end-to-end delivery
Two primary protocols located at this layer:
  Transmission Control Protocol (TCP)
    Transports data to another host
    Connection-oriented: reliable delivery
    Performs three-step handshake
  User Datagram Protocol (UDP)
    Fast but does not guarantee delivery of the packets
    Does not use a handshake process

## Slide 24: Internet / Network (3) Layer
Contains the following protocols:
  Internet Protocol (IP):
    Provides source and destination addressing
    Responsible for datagram fragmentation
    Routable
  Internet Control Message Protocol (ICMP):
    Provides error and control messages
    Used by Ping utility
  Address resolution protocol (ARP):
    Resolves IP to MAC addresses

## Slide 25: Network Access (2,1) Layer
Responsible for physical delivery of IP packets via frames
Ethernet frames use MAC addresses for identification:
  A physical address that uniquely identifies a particular NIC
  Could be
    Unicast
    Multicast
    Broadcast

## Slide 26: TCP/IP Protocol Stack

## Slide 27: TCP/IP Encapsulation

## Slide 28: TCP Header

## Slide 29: UDP Header

## Slide 30: IP Header

## Slide 31: Packets in practice

## Slide 32: TCP Ports in practice

## Slide 33: Break

## Slide 34: Creating a Network
What makes a network?
Systems
Switch/Hub
Router
Firewall
Wireless Access Point
Proxy
IDS/IPS
Forensics Appliance
What’s it look like?

## Slide 35: Creating a Network

## Slide 36: Packet Analyzing/Sniffing
All data on a network that is transmitted can be sniffed.
Web pages
Copying of files
Mail flow
DNS lookup
Network cards need to be put in “promiscuous mode” in order to listen to everything going on within the network.
Can be set with a literal “flip of a switch” via software
Network architecture needs to allow for “chatty” systems
Every node within a single LAN segment can see traffic of others on that segment

## Slide 37: Packet Analyzing/Sniffing

## Slide 38: Packet Analyzing/Sniffing

## Slide 39: NAT and Sniffing

## Slide 40: Packet Analyzing/Sniffing

## Slide 41: Sniffing Mitigation
By segmenting the Internal Network, you limit visibility of network sniffing, as well as provide a greater granularity of control over what access is needed.
Virtual Networking/VLAN allows for hosting multiple networks on a single network switch.
In order to sniff “ALL” VLANs, administrators set up a SPAN/Mirror port on the switch to plug into a network tap.
Does not prevent sniffing within a VLAN

## Slide 42: Why Sniff?
Sniffing captures ALL data on the wire.
Sniffing is used to troubleshoot network issues as well as inspect traffic to ensure it is not malicious. This practice is used in conjunction with Network Forensics tools and Intrusion Detection systems.
All “clear text” protocols are potential threat vectors
Some “encrypted text” protocols are as well depending on the strength of the encryption
IM conversations
POP Mail
SMTP Mail
DNS lookups
HTTP traffic
VOIP
Streaming video/music

## Slide 43: Why Sniff?

## Slide 44: Why Sniff?

## Slide 45: Summary
Know the six steps in the attacker’s methodology.
Explain the ethical hacker’s process.
Be familiar with the OSI model and each layer’s function.
Be familiar with the TCP/IP protocol stack.
Describe the four layers in the TCP/IP protocol.